## Slide 1: Bits, Bytes, and Integers
Professor Hugh C. Lauer CS-2011, Machine Organization and Assembly Language
(Slides include copyright materials from Computer Systems: A Programmer’s Perspective, by Bryant and O’Hallaron, and from The C Programming Language, by Kernighan and Ritchie)

## Slide 2: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
Summary
Reading Assignment: §2 thru §2.3

## Slide 3: Binary Representations
0.0V
0.5V
2.8V
3.3V
0
1
0

## Slide 4: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 5: Byte-oriented memory organization
Programs refer to virtual addresses
  Conceptually very large array of bytes
  Actually implemented with hierarchy of different memory types
  System provides address space private to particular “process”
    Program being executed
    Program can clobber its own data, but not that of others
Compiler + run-time system control allocation
  Where different program objects should be stored
  All allocation within single virtual address space
• • •
00•••0
FF•••F

## Slide 6: Machine words
Machine has “word size”
  Nominal size of integer-valued data
    Including addresses
  A lot of machines still use 32 bits (4 bytes) words
    Limits addresses to 4GB
    Becoming too small for memory-intensive applications
  High-end systems use 64 bits (8 bytes) words
    Potential address space ≈ 1.8 X 1019 bytes
    x86-64 machines support 48-bit addresses: 256 Terabytes
Machines support multiple data formats
  Fractions or multiples of word size
  Always integral number of bytes
Some machines still use 16 bits — 64 KB addresses

## Slide 7: Word-Oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 2 (16-bit), 4 (32-bit), or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 8: Data Representations
C Data Type | Typical 32-bit | Intel IA32 | x86-64
char | 1 | 1 | 1
short | 2 | 2 | 2
int | 4 | 4 | 4
long | 4 | 4 | 8
long long | 8 | 8 | 8
float | 4 | 4 | 4
double | 8 | 8 | 8
long double | 8 | 10/12 | 10/16
pointer | 4 | 4 | 8

## Slide 9: Byte Ordering
How should bytes within a multi-byte word be ordered in memory?
Conventions
  Big Endian: Sun, PPC Mac, Internet
    Least significant byte has highest address
  Little Endian: x86
    Least significant byte has lowest address
Trivia question:– When and how did the terms “big endian” and “little endian” enter the English language?

## Slide 10: Byte Ordering Example
Big Endian
  Least significant byte has highest address
Little Endian
  Least significant byte has lowest address
Example
  Variable x has 4-byte representation 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 11: Reading Byte-Reversed Listings
Address Instruction Code Assembly Rendition
8048365: 5b pop %ebx
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx
804836c: 83 bb 28 00 00 00 00 cmpl $0x0,0x28(%ebx)
Disassembly
  Text representation of binary machine code
  Generated by program that reads the machine code
Example Fragment
Deciphering Numbers
  Value: 0x12ab
  Pad to 32 bits: 0x000012ab
  Split into bytes: 00 00 12 ab
  Reverse: ab 12 00 00

## Slide 12: Examining Data Representations
Code to Print Byte Representation of Data
  Casting pointer to unsigned char * creates byte array
Printf directives:
%p: Print pointer
%x: Print Hexadecimal
typedef unsigned char *pointer;
void show_bytes(pointer start, int len){
int i;
for (i = 0; i < len; i++)
printf("%p\t0x%.2x\n",start+i, start[i]);
printf("\n");
}

## Slide 13: show_bytes Execution Example
int a = 15213;
printf("int a = 15213;\n");
show_bytes((pointer) &a, sizeof(int));
Result (Linux):
int a = 15213;
0x11ffffcb8 0x6d
0x11ffffcb9 0x3b
0x11ffffcba 0x00
0x11ffffcbb 0x00

## Slide 14: Representing Integers
Decimal: 15213
Binary: 0011 1011 0110 1101
Hex: 3 B 6 D
6D
3B
00
00
IA32, x86-64
3B
6D
00
00
Sun
int A = 15213;
93
C4
FF
FF
IA32, x86-64
C4
93
FF
FF
Sun
Two’s complement representation
(covered later)
int B = -15213;
long int C = 15213;
00
00
00
00
6D
3B
00
00
x86-64
3B
6D
00
00
Sun
6D
3B
00
00
IA32
Smallest memory addr at top →

## Slide 15: Representing Pointers
Different compilers & machines assign different locations to objects
int B = -15213;
int *P = &B;
x86-64
Sun
IA32
EF
FF
FB
2C
D4
F8
FF
BF
0C
89
EC
FF
FF
7F
00
00

## Slide 16: Representing Strings
char S[6] = "18243";
Strings in C
  Represented by array of characters
  Each character encoded in ASCII format
    Standard 7-bit encoding of character set
    Character “0” has code 0x30
      Digit i has code 0x30+i
  String should be null-terminated
    Final character = 0
Compatibility
  Byte ordering not an issue
Linux/Alpha
Sun
31
38
32
34
33
00
31
38
32
34
33
00

## Slide 17: Questions?

## Slide 18: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
Summary
Reading Assignment: §2.1.7–§2.1.10

## Slide 19: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And
A&B = 1 when both A=1 and B=1
Or
A|B = 1 when either A=1 or B=1
Not
~A = 1 when A=0
Exclusive-Or (Xor)
A^B = 1 when either A=1 or B=1, but not both

## Slide 20: Application of Boolean Algebra
Applied to Digital Systems by Claude Shannon
  1937 MIT Master’s Thesis
  Reason about networks of relay switches
    Encode closed switch as 1, open switch as 0
A
~A
~B
B
Connection when
A&~B | ~A&B
A&~B
~A&B
= A^B

## Slide 21: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01101001
| 01010101
01101001
^ 01010101
~ 01010101
01000001
01111101
00111100
10101010

## Slide 22: Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j ∈ A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 23: Bit-Level Operations in C
Operations available in C:– &, |, ~, ^
  Apply to any “integral” data type–
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 ➙ 0xBE
    ~010000012 ➙ 101111102
  ~0x00 ➙ 0xFF
    ~000000002 ➙ 111111112
  0x69 & 0x55 ➙ 0x41
    011010012 & 010101012 ➙ 010000012
  0x69 | 0x55 ➙ 0x7D
    011010012 | 010101012 ➙ 011111012

## Slide 24: Contrast: Logic Operations in C
Contrast to logical operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 ➙ 0x00
  !0x00 ➙ 0x01
  !!0x41 ➙ 0x01
  0x69 && 0x55 ➙ 0x01
  0x69 || 0x55 ➙ 0x01
  p && *p p && p -> f
  (avoids null pointer access)

## Slide 25: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
      Throw away extra bits on left
    Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on right
Undefined Behavior
  Shift amount < 0 or ≥ word size
  Different machines behave differently
01100010
Argument x
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
Argument x
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 26: Questions?

## Slide 27: Today: bits, bytes, and integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
Summary
Reading Assignment: §2.2

## Slide 28: Encoding integers
Unsigned
Two’s Complement
Sign Bit
§ 2.2.2 in Bryant and O’Hallaron
§ 2.2.3 in Bryant and O’Hallaron

## Slide 29: Encoding integers
C short 2 bytes long
Sign bit
  For 2’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative
short int x = 15213;
short int y = -15213;
Unsigned
Two’s Complement
Sign
Bit

## Slide 30: Encoding example (continued)
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011

## Slide 31: Numeric ranges
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1
Two’s Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
Other Values
  Minus 1
    111…1
Values for W = 16

## Slide 32: Values for different word sizes
Observations
  |TMin | = TMax + 1
    Asymmetric range
  UMax = 2 * TMax + 1
C Programming
  #include <limits.h>
  Declares constants, e.g.,
    ULONG_MAX
    LONG_MAX
    LONG_MIN
  Values platform specific

## Slide 33: Unsigned & Signed Numeric Values
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
 Can Invert Mappings
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s comp integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7

## Slide 34: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
Summary
Reading Assignment: §2.2 (continued)

## Slide 35: (Review) Encoding integers
Two’s Complement Values
  TMin = –2w–1
    100…0
  TMax = 2w–1 – 1
    011…1
Unsigned
Two’s Complement
Sign Bit
Unsigned Values
  UMin = 0
    000…0
  UMax = 2w – 1
    111…1

## Slide 36: (Review) Signed vs. Unsigned
0
Tmin
1
2
Tmax
Umax
Positive ints
0 .. Tmax
Negative ints
–1 .. Tmin
Umax/2
Unsigned (Umax/2) .. Umax
–1
Unsigned 0 .. (Umax/2)

## Slide 37: Mapping Between Signed & Unsigned
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X
Mappings between unsigned and two’s complement numbers:–
keep same bit representations and reinterpret
U2T
U2B
B2T
Two’s Complement
Unsigned
Maintain Same Bit Pattern
ux
x
X

## Slide 38: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
U2T
T2U

## Slide 39: Mapping Signed  Unsigned
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
=
+/- 16

## Slide 40: Relation between Signed & Unsigned
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
ux
x
w–1
0
Large negative weight
becomes
Large positive weight
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
x
ux
X

## Slide 41: Conversion Visualized
0
TMax
TMin
–1
–2
0
UMax
UMax – 1
TMax
TMax + 1
2’s Complement Range
Unsigned
Range
2’s Comp.  Unsigned
  Ordering Inversion
  Negative  Big Positive

## Slide 42: Signed vs. unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and function calls
    tx = ux;
    uy = ty;

## Slide 43: Casting Surprises
Expression Evaluation
  If there is a mix of unsigned and signed in single expression, signed values implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32: TMIN = -2,147,483,648 , TMAX = 2,147,483,647
Constant1 Constant2 Relation Evaluation
  0 0U
  -1 0
  -1 0U
  2147483647 -2147483647-1
  2147483647U -2147483647-1
  -1 -2
  (unsigned)-1 -2
  2147483647 2147483648U
  2147483647 (int) 2147483648U
  == unsigned
  < signed
  > unsigned
  > signed
  < unsigned
  > signed
  > unsigned
  < unsigned
  > signed

## Slide 44: Code Security Example
Similar to code found in FreeBSD’s implementation of getpeername
There are legions of smart people trying to find vulnerabilities in programs
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}

## Slide 45: Typical Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, MSIZE);
printf("%s\n", mybuf);
}

## Slide 46: Malicious Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, -MSIZE);
. . .
}
/* Declaration of library function memcpy */
void *memcpy(void *dest, void *src, size_t n);
size_t is defined as an unsigned integer
(K&R §A7.4.8) <stddef.h>

## Slide 47: Summary Casting Signed ↔ Unsigned: Basic Rules
Bit pattern is maintained
But reinterpreted
Can have unexpected effects: adding or subtracting 2w
Expression containing signed and unsigned int
  int is cast to unsigned!!

## Slide 48: Questions?

## Slide 49: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
Summary
Reading Assignment: §2.2 (continued)

## Slide 50: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 51: Sign Extension Example
Converting from smaller to larger integer data type
C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 52: Summary: Expanding, Truncating: Basic Rules
Expanding (e.g., short int to int)
  Unsigned: zeros added
  Signed: sign extension
  Both yield expected result
Truncating (e.g., unsigned to unsigned short)
  Unsigned/signed: bits are truncated
  Result reinterpreted
  Unsigned: mod operation
  Signed: similar to mod
  For small numbers yields expected behavior

## Slide 53: Truncating — Illustration
For unsigned numbers:–
  Equivalent to dividing by 2k and keeping the remainder
    i.e., truncate(x, k) = x mod 2k
For signed numbers:–
  Same bit result …
  … but truncated number may have different sign!
• • •
X
X 
• • •
• • •
w
w
k

## Slide 54: Today: Bits, Bytes, and Integers
Representing information as bits
Bit-level manipulations
Integers
  Representation: unsigned and signed
  Conversion, casting
  Expanding, truncating
  Addition, negation, multiplication, shifting
Summary
Reading Assignment: §2.3

## Slide 55: Negation: Complement & Increment
Claim: Following Holds for 2’s Complement
  ~x + 1 == -x
Complement
  Observation: ~x + x == 1111…111 == -1
Complete Proof?
1
0
0
1
0
1
1
1
x
0
1
1
0
1
0
0
0
~x
+
1
1
1
1
1
1
1
1
-1

## Slide 56: Complement & Increment Examples
x = 15213
x = 0

## Slide 57: Unsigned Addition
Standard Addition Function
  Ignores carry output
Implements Modular Arithmetic
  s = UAddw(u , v) = u + v mod 2w
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
UAddw(u , v)

## Slide 58: Visualizing (Mathematical) Integer Addition
Integer Addition
  4-bit integers u, v
  Compute true sum Add4(u , v)
  Values increase linearly with u and v
  Forms planar surface
Add4(u , v)
u
v

## Slide 59: Visualizing Unsigned Addition
Wraps Around
  If true sum ≥ 2w
  At most once
0
2w
2w+1
UAdd4(u , v)
u
v
True Sum
Modular Sum
Overflow
Overflow

## Slide 60: Mathematical Properties
Modular Addition Forms an Abelian Group
  Closed under addition
    0  UAddw(u , v)  2w –1
  Commutative
    UAddw(u , v) = UAddw(v , u)
  Associative
    UAddw(t, UAddw(u , v)) = UAddw(UAddw(t, u ), v)
  0 is additive identity
    UAddw(u , 0) = u
  Every element has additive inverse
    Let UCompw (u ) = 2w – u UAddw(u , UCompw (u )) = 0

## Slide 61: Two’s Complement Addition
TAdd and UAdd have Identical Bit-Level Behavior
  Signed vs. unsigned addition in C:
  int s, t, u, v;
  s = (int) ((unsigned) u + (unsigned) v);
  t = u + v
  Will give s == t
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
Discard Carry: w bits
TAddw(u , v)

## Slide 62: TAdd Overflow
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
–2w –1–1
–2w
0
2w –1
2w–1
True Sum
TAdd Result
1 000…0
1 011…1
0 000…0
0 100…0
0 111…1
100…0
000…0
011…1
PosOver
NegOver

## Slide 63: Visualizing 2’s Complement Addition
Values
  4-bit two’s comp.
  Range from -8 to +7
Wraps Around
  If sum  2w–1
    Becomes negative
    At most once
  If sum < –2w–1
    Becomes positive
    At most once
TAdd4(u , v)
u
v
PosOver
NegOver

## Slide 64: Characterizing TAdd
Functionality
  True sum requires w+1 bits
  Drop off MSB
  Treat remaining bits as 2’s comp. integer
(NegOver)
(PosOver)
u
v
< 0
> 0
< 0
> 0
Negative Overflow
Positive Overflow
TAdd(u , v)
2w
2w

## Slide 65: Mathematical Properties of TAdd
Isomorphic Group to unsigneds with UAdd
  TAddw(u , v) = U2T(UAddw(T2U(u ), T2U(v)))
    Since both have identical bit patterns
Two’s Complement Under TAdd Forms a Group
  Closed, Commutative, Associative, 0 is additive identity
  Every element has additive inverse

## Slide 66: Questions?

## Slide 67: Multiplication — shifting and adding
15213
× 2011
15213
152130
30426000
30593343

## Slide 68: Multiplication in Binary

## Slide 69: Multiplication in Binary – mod 2w
Overflow bits truncated

## Slide 70: Multiplication in Binary
Any difference between unsigned and twos complement?
A:– No!
  Same bit pattern
  Different interpretation
  Different overflows

## Slide 71: Multiplication performance
10 or more machine cycles
  In modern processors
Multiply-and-Add instruction
Easily pipelined
  E.g., dot product

## Slide 72: Compiler optimizations
Small, constant multipliers
  E.g., array indexes
Shift instructions followed by adds
Specialized instructions

## Slide 73: Power-of-2 Multiply with Shift
Operation
  u << k gives u * 2k
  Both signed and unsigned
Examples
  u << 3 == u * 8
  (u << 5) – (u << 3)== u * 24
  Most machines shift and add faster than multiply
    gcc generates this code automatically
• • •
0
0
1
0
0
0
•••
u
2k
*
u · 2k
True Product: w+k bits
Operands: w bits
Discard k bits: w bits
UMultw(u , 2k)
•••
k
• • •
0
0
0
•••
TMultw(u , 2k)
0
0
0
•••
•••

## Slide 74: Compiled Multiplication Code
leal (%eax,%eax,2), %eax
sall $2, %eax
C compiler automatically generates shift/add code when multiplying by constant
int mul12(int x)
{
return x*12;
}
t <- x+x*2
return t << 2;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 75: Questions?

## Slide 76: Division — subtracting and shifting
______ 13 )15213
13213
2200 1300
910 910
3
1
1
1
7
0

## Slide 77: Binary Division
Similar principle:–
  Subtract divisor from high-order bits of dividend
  Shift, bring down next bit
  Repeat
Very costly in number of cycles
  30 or more for integer divide
Not very amenable to pipelining
Highly specialized designs
  Mostly implemented in Floating Point arithmetic units

## Slide 78: Unsigned Power-of-2 Divide with Shift
Quotient of Unsigned by Power of 2
  u >> k gives  u / 2k 
  Uses logical shift
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
0
0
•••
•••
 u / 2k 
•••
Result:
.
Binary Point
0
0
0
0
•••
0

## Slide 79: Compiled Unsigned Division Code
shrl $3, %eax
Uses logical shift for unsigned
For Java Users
  Logical shift written as >>>
unsigned udiv8(unsigned x)
{
return x/8;
}
# Logical shift
return x >> 3;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 80: Signed Power-of-2 Divide with Shift
Quotient of Signed by Power of 2
  x >> k gives  x / 2k 
  Uses arithmetic shift
  Rounds wrong direction when u < 0
0
0
1
0
0
0
•••
x
2k
/
x / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
•••
•••
RoundDown(x / 2k)
•••
Result:
.
Binary Point
0
•••

## Slide 81: Correct Power-of-2 Divide
Quotient of Negative Number by Power of 2
  Want  x / 2k  (Round Toward 0)
  Compute as  (x+2k-1)/ 2k 
    In C: (x + (1<<k)-1) >> k
    Biases dividend toward 0
Case 1: No rounding
Divisor:
Dividend:
0
0
1
0
0
0
•••
u
2k
/
 u / 2k 
•••
k
1
•••
0
0
0
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
1
1
•••
1
•••
1
1
1
•••
    Biasing has no effect

## Slide 82: Correct Power-of-2 Divide (Cont.)
Divisor:
Dividend:
Case 2: Rounding
0
0
1
0
0
0
•••
x
2k
/
 x / 2k 
•••
k
1
•••
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
•••
•••
    Biasing adds 1 to final result
•••
Incremented by 1
Incremented by 1

## Slide 83: Compiled Signed Division Code
testl %eax, %eax
js L4
L3:
sarl $3, %eax
ret
L4:
addl $7, %eax
jmp L3
Uses arithmetic shift for int
For Java Users
  Arith. shift written as >>
int idiv8(int x)
{
return x/8;
}
if x < 0
x += 7;
# Arithmetic shift
return x >> 3;
C Function
Compiled Arithmetic Operations
Explanation

## Slide 84: Questions?

## Slide 85: Arithmetic: Basic Rules
Addition:
  Unsigned/signed: Normal addition followed by truncate, same operation on bit level
  Unsigned: addition mod 2w
    Mathematical addition + possible subtraction of 2w
  Signed: modified addition mod 2w (result in proper range)
    Mathematical addition + possible addition or subtraction of 2w
Multiplication:
  Unsigned/signed: Normal multiplication followed by truncate, same operation on bit level
  Unsigned: multiplication mod 2w
  Signed: modified multiplication mod 2w (result in proper range)

## Slide 86: Arithmetic: Basic Rules
Unsigned ints, 2’s complement ints are isomorphic rings: isomorphism = casting
Left shift
  Unsigned/signed: multiplication by 2k
  Always logical shift
Right shift
  Unsigned: logical shift, div (division + round to zero) by 2k
  Signed: arithmetic shift
    Positive numbers: div (division + round to zero) by 2k
    Negative numbers: div (division + round away from zero) by 2k Use biasing to fix

## Slide 87: Questions?

## Slide 88: Today: Integers
Representation: unsigned and signed
Conversion, casting
Expanding, truncating
Addition, negation, multiplication, shifting
Summary

## Slide 89: Properties of Unsigned Arithmetic
Unsigned Multiplication with Addition Forms Commutative Ring
  Addition is commutative group
  Closed under multiplication
    0  UMultw(u , v)  2w –1
  Multiplication Commutative
    UMultw(u , v) = UMultw(v , u)
  Multiplication is Associative
    UMultw(t, UMultw(u , v)) = UMultw(UMultw(t, u ), v)
  1 is multiplicative identity
    UMultw(u , 1) = u
  Multiplication distributes over addtion
    UMultw(t, UAddw(u , v)) = UAddw(UMultw(t, u ), UMultw(t, v))

## Slide 90: Properties of Two’s Comp. Arithmetic
Isomorphic Algebras
  Unsigned multiplication and addition
    Truncating to w bits
  Two’s complement multiplication and addition
    Truncating to w bits
Both Form Rings
  Isomorphic to ring of integers mod 2w
Comparison to (Mathematical) Integer Arithmetic
  Both are rings
  Integers obey ordering properties, e.g.,
    u > 0  u + v > v
    u > 0, v > 0  u · v > 0
  These properties are not obeyed by two’s comp. arithmetic
    TMax + 1 == TMin
    15213 * 30426 == -10030 (16-bit words)

## Slide 91: Why Should I Use Unsigned?
Don’t Use Just Because Number Nonnegative
  Easy to make mistakes
    unsigned i;
    for (i = cnt-2; i >= 0; i--)
    a[i] += a[i+1];
  Can be very subtle
    #define DELTA sizeof(int)
    int i;
    for (i = CNT; i-DELTA >= 0; i-= DELTA)
    . . .
Do Use When Performing Modular Arithmetic
  Multiprecision arithmetic
Do Use When Using Bits to Represent Sets
  Logical right shift, no sign extension

## Slide 92: Integer C Puzzles
x < 0  ((x*2) < 0)
ux >= 0
x & 7 == 7  (x<<30) < 0
ux > -1
x > y  -x < -y
x * x >= 0
x > 0 && y > 0  x + y > 0
x >= 0  -x <= 0
x <= 0  -x >= 0
(x|-x)>>31 == -1
ux >> 3 == ux/8
x >> 3 == x/8
x & (x-1) != 0
int x = foo();
int y = bar();
unsigned ux = x;
unsigned uy = y;
Initialization

## Slide 93: On the Design
All slides are in Powerpoint 2007 (mix of PC and Mac versions)
Probably could be edited using Powerpoint 2003 plus
  File format plugin
  Calibri font
  I would still recommend to use 2007 for editing
Design is suitable for printing out slides
  Only light colors, in particular for boxes
Some slides have covered areas (that disappear later) suitable for quizzing in class
The design follows the Small Guide to Giving Presentations
Next slides: Color/format conventions

## Slide 94: System-Level I/O CS-2011: Introduction to Machine Organization and Assembly Language 14th Lecture, Oct. 12, 2010
Instructor:
Hugh C. Lauer
Style for title slides

## Slide 95: Today
Unix I/O
RIO (robust I/O) package
Metadata, sharing, and redirection
Standard I/O
Conclusions and examples
Style for outlining

## Slide 96: Style for Figure Labels
Capitalize only the first word in each figure label
  E.g., “Payload and padding”, not “Payload and Padding”, or “payload and padding”
  This is the same style convention that we used in CS:APP2e.
Size
Format of
allocated and
free blocks
Payload and
padding
a = 1: Allocated block
a = 0: Free block
Size: Total block size
Payload: Application data
(allocated blocks only)
a
Size
a
Boundary tag
(footer)
Header

## Slide 97: Style for Code
/*
* hello.c - Pthreads "hello, world" program
*/
#include "csapp.h"
void *thread(void *vargp);
int main() {
pthread_t tid;
Pthread_create(&tid, NULL, thread, NULL);
Pthread_join(tid, NULL);
exit(0);
}
/* thread routine */
void *thread(void *vargp) {
printf("Hello, world!\n");
return NULL;
}

## Slide 98: Style for Code and Alternative Code
C Code
int fact_do(int x)
{
int result = 1;
do {
result *= x;
x = x-1;
} while (x > 1);
return result;
}
Goto Version
int fact_goto(int x)
{
int result = 1;
loop:
result *= x;
x = x-1;
if (x > 1)
goto loop;
return result;
}

## Slide 99: Style for Assembly Code: Version I
int absdiff(int x, int y)
{
int result;
if (x > y) {
result = x-y;
} else {
result = y-x;
}
return result;
}
absdiff:
pushl %ebp
movl %esp, %ebp
movl 8(%ebp), %edx
movl 12(%ebp), %eax
cmpl %eax, %edx
jle .L7
subl %eax, %edx
movl %edx, %eax
.L8:
leave
ret
.L7:
subl %edx, %eax
jmp .L8
Body1
Setup
Finish
Body2

## Slide 100: Style for Assembly Code: Version II
struct rec {
int i;
int a[3];
int *p;
};
# %edx = r
movl (%edx),%ecx # r->i
leal 0(,%ecx,4),%eax # 4*(r->i)
leal 4(%edx,%eax),%eax # r+4+4*(r->i)
movl %eax,16(%edx) # Update r->p
void
set_p(struct rec *r)
{
r->p =
&r->a[r->i];
}

## Slide 101: Linux Command Prompt
linux> ./badcnt
BOOM! cnt=198841183
linux> ./badcnt
BOOM! cnt=198261801
linux> ./badcnt
BOOM! cnt=198269672

## Slide 102: Stack and Registers
Return addr
Saved
registers
+
Local
variables
Argument
build
Old %ebp
Arguments
Caller
Frame
%ebp
%esp
%eax
%edx
%ecx
%ebx
%esi
%edi
%esp
%ebp
Caller-save
Callee-save
Special

## Slide 103: Bar Plot
Chart: 
| 256 | 512 | 1k | 2k | 4k | 8k | 16k | 32k | 64k | 128k | 256k
lower1 | 0.000266 | 0.001033 | 0.004066 | 0.016678 | 0.067395 | 0.27087 | 1.0825 | 4.9645 | 20.0633 | 80.1428 | 341.5956
lower2 | 6e-06 | 1.2e-05 | 2.4e-05 | 4.8e-05 | 9.5e-05 | 0.000191 | 0.000382 | 0.000808 | 0.001615 | 0.003229 | 0.006694
CPU Seconds
String Length

## Slide 104: Tables
Machine | Nocona | Core 2
rfact | 15.5 | 6.0
fact | 10.0 | 3.0
Cycles per element (or per mult)
Method | Int (add/mult) |  | Float (add/mult) | 
combine4 | 2.2 | 10.0 | 5.0 | 7.0
unroll2 | 1.5 | 10.0 | 5.0 | 7.0
unroll2-ra | 1.56 | 5.0 | 2.75 | 3.62
bound | 1.0 | 1.0 | 2.0 | 2.0
Some instructions take > 1 cycle, but can be pipelined
  Instruction Latency Cycles/Issue
  Load / Store 5 1
  Integer Multiply 10 1
  Integer/Long Divide 36/106 36/106
  Single/Double FP Multiply 7 2
  Single/Double FP Add 5 2
  Single/Double FP Divide 32/46 32/46

## Slide 105: Color Palette
Boxes/areas:
  Assembly, memory, …
  Linux, memory, …
  Code, …
  Code, registers, …
  Registers, …
  Memory, …
  Memory, …
Occasionally, use darker versions of above colors
Text:
  Emphasizing something in the text
  Comments inside yellow code boxes