## Slide 1: Course Theme: Abstraction vs. Reality
Professor Hugh C. Lauer CS-2011, Machine Organization and Assembly Language
(Slides include copyright materials from Computer Systems: A Programmer’s Perspective, by Bryant and O’Hallaron, and from The C Programming Language, by Kernighan and Ritchie)

## Slide 2: Course Theme: Abstraction is good but don’t forget reality
Most CS courses emphasize abstraction
  Abstract data types
  Asymptotic analysis
Abstractions have limits
  Especially in the presence of bugs
  Need to understand details of underlying implementations
Useful outcomes
  Become more effective programmers
    Able to find and eliminate bugs efficiently
    Able to understand and tune for program performance
  Prepare for later “systems” classes in CS & ECE
    Compilers, Operating Systems, Networks, Computer Architecture, Embedded Systems

## Slide 3: Great Reality #1: Ints are not integers, floats are not reals
Example 1: Is x2 ≥ 0?
  Float’s: Yes!
  Int’s:
    40000 * 40000 ➙ 1,600,000,000
    50000 * 50000 ➙ ??
Example 2: Is (x + y) + z = x + (y + z)?
  Unsigned & Signed Int’s: Yes!
  Float’s:
    (1e20 + -1e20) + 3.14 --> 3.14
    1e20 + (-1e20 + 3.14) --> ??
Source: xkcd.com/571
-352,516,352

## Slide 4: Code security example
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
Similar to code found in FreeBSD’s implementation of getpeername()
There are legions of smart people trying to find vulnerabilities in programs

## Slide 5: Typical usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, MSIZE);
printf("%s\n", mybuf);
}

## Slide 6: Malicious usage
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, -MSIZE);
. . .
}
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
This line turns out to be toxic!

## Slide 7: Computer arithmetic
Does not generate random values
  Arithmetic operations have important mathematical properties
Cannot assume all “usual” mathematical properties
  Due to finiteness of representations
  Integer operations satisfy “ring” properties
    Commutative, associative, distributive
  Floating point operations satisfy “ordering” properties
    Monotonicity, values of signs
Observation
  Need to understand which abstractions apply in which contexts
  Important issues for compiler writers and serious application programmers

## Slide 8: Great Reality #2: You’ve got to know assembly language
Chances are, you’ll never write programs in assembly
  Compilers are much better & more patient than you are
But: Understanding assembly is key to machine-level execution model
  Behavior of programs in presence of bugs
    High-level language models break down
  Tuning program performance
    Understand optimizations done / not done by the compiler
    Understanding sources of program inefficiency
  Implementing system software
    Compiler has machine code as target
    Operating systems must manage process state
  Creating / fighting malware
    x86 assembly is the language of choice!

## Slide 9: Assembly code example
Time Stamp Counter
  Special 64-bit register in Intel-compatible machines
  Incremented every clock cycle
  Read with rdtsc instruction
Application
  Measure time (in clock cycles) required by procedure
double t;
start_counter();
P();
t = get_counter();
printf("P required %f clock cycles\n", t);

## Slide 10: Code to read counter
Write small amount of assembly code using GCC’s asm facility
Inserts assembly code into machine code generated by compiler
static unsigned cyc_hi = 0;
static unsigned cyc_lo = 0;
/* Set *hi and *lo to the high and low order bits
of the cycle counter.
*/
void access_counter(unsigned *hi, unsigned *lo)
{
asm("rdtsc; movl %%edx,%0; movl %%eax,%1"
: "=r" (*hi), "=r" (*lo)
:
: "%edx", "%eax");
}
Notes: GCC Extended assembly syntax
asm( assembler syntax
: output operands /*optional */
: input operands /* optional */
: list of clobbered registers /* optional */
);

## Slide 11: Great Reality #3: Memory matters Random access memory is an unphysical abstraction
Memory is not unbounded
  It must be allocated and managed
  Many applications are memory dominated
Memory referencing bugs especially pernicious
  Effects are distant in both time and space
Memory performance is not uniform
  Cache and virtual memory effects can greatly affect program performance
  Adapting program to characteristics of memory system can lead to major speed improvements

## Slide 12: Memory referencing bug example
double fun(int i)
{
volatile double d[1] = {3.14};
volatile long int a[2];
a[i] = 1073741824; /* Possibly out of bounds */
return d[0];
}
Result is architecture specific
fun(0) ➙ 3.14
fun(1) ➙ 3.14
fun(2) ➙ 3.1399998664856
fun(3) ➙ 2.00000061035156
fun(4) ➙ 3.14, then segmentation fault

## Slide 13: Memory referencing bug example
Location accessed by fun(i)
Explanation:
Saved State | 4
d7 ... d4 | 3
d3 ... d0 | 2
a[1] | 1
a[0] | 0
double fun(int i)
{
volatile double d[1] = {3.14};
volatile long int a[2];
a[i] = 1073741824; /* Possibly out of bounds */
return d[0];
}
fun(0) ➙ 3.14
fun(1) ➙ 3.14
fun(2) ➙ 3.1399998664856
fun(3) ➙ 2.00000061035156
fun(4) ➙ 3.14, then segmentation fault

## Slide 14: Memory referencing errors
C and C++ do not provide any memory protection
  Out of bounds array references
  Invalid pointer values
  Abuses of malloc()/free()
Can lead to nasty bugs
  Whether or not bug has any effect depends on system and compiler
  Action at a distance
    Corrupted object logically unrelated to one being accessed
    Effect of bug may be first observed long after it is generated
How can I deal with this?
  Program in Java, Ruby. or ML
  Understand what possible interactions may occur
  Use or develop tools to detect referencing errors (e.g. Valgrind)

## Slide 15: Great Reality #4: More to performance than asymptotic complexity
Constant factors matter too!
And even exact op count does not predict performance
  Easily see 10:1 performance range depending on how code written
  Must optimize at multiple levels: algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs compiled and executed
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 16: Memory system performance example
Hierarchical memory organization
Performance depends on access patterns
  Including how step through multi-dimensional array
void copyji(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (j = 0; j < 2048; j++)
for (i = 0; i < 2048; i++)
dst[i][j] = src[i][j];
}
void copyij(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (i = 0; i < 2048; i++)
for (j = 0; j < 2048; j++)
dst[i][j] = src[i][j];
}
21 times slower (Pentium 4)

## Slide 17: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11 | s12 | s13 | s14 | s15 | s16 | s32 | s64
64M | 4029.59 | 2752.75 | 2159.29 | 1710.75 | 1391.48 | 1176.29 | 1015.77 | 890.72 | 845.57 | 805.46 | 773.78 | 757.94 | 727.91 | 712.66 | 705.63 | 701.98 | 598.19 | 601.22
32M | 4029.36 | 2752.39 | 2160.62 | 1710.98 | 1391.5 | 1176.54 | 1016.71 | 891.8 | 846.98 | 807.22 | 775.18 | 760.41 | 730.74 | 714.98 | 709.26 | 708.88 | 608.99 | 607.39
16M | 4040.1 | 2788.42 | 2188.92 | 1742.97 | 1421.69 | 1201.31 | 1038.37 | 911.7 | 870.39 | 835.31 | 809.25 | 798.05 | 780.28 | 778.37 | 787.2 | 744.13 | 633.53 | 608.86
8M | 4374.01 | 3610.74 | 3002.03 | 2492.39 | 2131.04 | 1821.71 | 1564.14 | 1414.18 | 1404.78 | 1408.59 | 1423.67 | 1456.86 | 1499.61 | 1600.13 | 1667.47 | 1231.7 | 1078.97 | 1026.03
4M | 4642.47 | 4583.8 | 4074.93 | 3557.51 | 3337.59 | 2898.78 | 2535.22 | 2248.83 | 2227.41 | 2203.98 | 2187.29 | 2164.18 | 2156.96 | 2148.52 | 2146.83 | 2131.36 | 2038.29 | 2060.87
2M | 4674.06 | 4659.06 | 4153.1 | 4016.4 | 3540.78 | 3027.05 | 2625.06 | 2321.73 | 2306.4 | 2292.86 | 2282.38 | 2270.35 | 2264.14 | 2259.8 | 2260.46 | 2261.54 | 2224.92 | 2431.58
1M | 4673.77 | 4656.98 | 4156.32 | 4012.65 | 3535.85 | 3021.82 | 2623.08 | 2318.19 | 2303.72 | 2291.55 | 2280.42 | 2270.24 | 2264.82 | 2261.86 | 2261.31 | 2271.41 | 2237.27 | 2432.74
512K | 4673 | 4658.05 | 4267.3 | 4052.55 | 3730.88 | 3236.67 | 2839.93 | 2527.15 | 2513.25 | 2503.12 | 2494.19 | 2517.44 | 2523.1 | 2551.67 | 2555.53 | 2477.41 | 2420.17 | 2590.64
256K | 4672.31 | 4645.58 | 4300.1 | 4091.3 | 3890.2 | 3175.38 | 2748.26 | 2351.27 | 2518.38 | 2627.49 | 2644.71 | 2646.45 | 2690.79 | 2715.46 | 2762.7 | 2445.48 | 2440.11 | 2560.87
128K | 4669.89 | 4661.44 | 4661.75 | 4570.55 | 4453.42 | 4070.1 | 3626.17 | 2349.05 | 3332.47 | 3318.78 | 3328.21 | 3312.1 | 3351.75 | 3197.56 | 3342.59 | 3330.51 | 3335.4 | 3374.9
64K | 4664.69 | 4647.96 | 4646.51 | 4575.1 | 4473.68 | 4218.51 | 3642.61 | 3334.78 | 3395.82 | 3398 | 3403.08 | 3411.87 | 3395.99 | 3299.01 | 4287.45 | 3416.74 | 3389.13 | 3374.16
32K | 4654.62 | 4624.5 | 4631.69 | 4615.62 | 4600.39 | 4585.6 | 4572.8 | 4809.1 | 4803.13 | 4789.7 | 4790.97 | 4784.65 | 4754.23 | 4768.54 | 4750.25 | 4742.01 | 6545.16 | 6408.41
Intel Core i7
2.67 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
Fig 6.41 p. 641

## Slide 18: Example Matrix Multiplication
Standard desktop computer, vendor compiler, using optimization flags
Both implementations have exactly the same operations count (2n3)
What is going on?
Matrix-Matrix Multiplication (MMM) on 2 x Core 2 Duo 3 GHz (double precision)
Gflop/s
160x
Triple loop
Best code (K. Goto)

## Slide 19: MMM Plot: Analysis
Matrix-Matrix Multiplication (MMM) on 2 x Core 2 Duo 3 GHz
Gflop/s
Memory hierarchy and other optimizations: 20x
Vector instructions: 4x
Multiple threads: 4x
Reason for 20x: Blocking or tiling, loop unrolling, array scalarization, instruction scheduling, search to find best choice
Effect: fewer register spills, L1/L2 cache misses, and TLB misses

## Slide 20: Great Reality #5: Computers do more than execute programs
They need to get data in and out
  I/O system critical to program reliability and performance
They communicate with each other over networks
  Many system-level issues arise in presence of network
    Concurrent operations by autonomous processes
    Coping with unreliable media
    Cross platform compatibility
    Complex performance issues

## Slide 21: Questions? Comments?