## Slide 1: Cache Memories
Professor Hugh C. Lauer CS-2011, Machine Organization and Assembly Language
(Slides include copyright materials from Computer Systems: A Programmer’s Perspective, by Bryant and O’Hallaron, and from The C Programming Language, by Kernighan and Ritchie)

## Slide 2: Cache Overview in Microprocessors
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 3: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 4: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 5: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 6: Today
Cache memory organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality
Reading Assignment: §6.1 – §6.5

## Slide 7: Cache Memories in Processors
Cache memories are small, fast SRAM-based memories managed automatically in hardware.
  Hold frequently accessed blocks of main memory
Processor looks first for data in caches (e.g., L1, L2, and L3), then in main memory.
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
Processor chip
System bus
Memory bus
Cache
memories

## Slide 8: Caching issues
How do you know whether an item is in the cache or not?
  I.e., how do you find it quickly?
What do you do when the item you want is not in the cache
  And how do you make space for it?

## Slide 9: Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 10: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 11: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 12: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag

## Slide 13: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
No match: old line is evicted and replaced

## Slide 14: Direct-Mapped Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=4 sets, E=1 Blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
?
?
v
Tag
Block
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
1
0
M[0-1]
Set 0
Set 1
Set 2
Set 3

## Slide 15: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 bytes = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_cols(double a[16][16])
{
int i, j;
double sum = 0;
for (j = 0; j < 16; j++)
for (i = 0; i < 16; i++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 16: Questions?

## Slide 17: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set

## Slide 18: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag

## Slide 19: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 20: 2-Way Set Associative Cache Simulation
M=16 byte addresses, B=2 bytes/block,
S=2 sets, E=2 blocks/set
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
?
?
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 21: A Higher Level Example
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
for (i = 0; i < 16; i++)
for (j = 0; j < 16; j++)
sum += a[i][j];
return sum;
}
32 bytes = 4 doubles
assume: cold (empty) cache,
a[0][0] goes here
int sum_array_rows(double a[16][16])
{
int i, j;
double sum = 0;
  for (j = 0; j < 16; j++)
for (i = 0; i < 16; i++)
sum += a[i][j];
return sum;
}
blackboard
Ignore the variables sum, i, j

## Slide 22: What about writes?
Multiple copies of data exist:
  L1, L2, Main Memory, Disk
What to do on a write-hit?
  Write-through (write immediately to memory)
  Write-back (defer write to memory until replacement of line)
    Need a dirty bit (meaning: line different from memory or not)
What to do on a write-miss?
  Write-allocate (load into cache, update line in cache)
    Good if more writes to the location follow
  No-write-allocate (writes immediately to memory)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate

## Slide 23: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 KB each, 8-way,
  Access: 4 cycles
L2 unified* cache:
  256 KB, 8-way,
  Access: 11 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 30-40 cycles
Block size: 64 bytes for all caches.
* “Unified” = instructions + data

## Slide 24: Cache Performance
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    1-2 clock cycle for L1
    5-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 25: Cache Performance (continued)
Average access time =
  Hit time + miss_rate × miss penalty
Example
  Hit time for L1 cache = 1 cycle
  Miss penalty for L1 cache = 10 cycles
  Miss rate = 10%
   Average access time = 1 + 0.1 * 10 = 2
Example 2
  Miss rate = 1%
   Average access time = 1 + 0.01 * 10 = 1.1

## Slide 26: Think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 27: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories.
See especially: §6.5

## Slide 28: Questions?

## Slide 29: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality
See: §6.6

## Slide 30: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 31: Memory Mountain Test Function
long data[MAXELEMS]; /* Global array to traverse */
/* test - Iterate over first "elems" elements of
* array “data” with stride of "stride", using
* using 4x4 loop unrolling.
*/
int test(int elems, int stride) {
long i, sx2=stride*2, sx3=stride*3, sx4=stride*4;
long acc0 = 0, acc1 = 0, acc2 = 0, acc3 = 0;
long length = elems, limit = length - sx4;
/* Combine 4 elements at a time */
for (i = 0; i < limit; i += sx4) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+stride];
acc2 = acc2 + data[i+sx2];
acc3 = acc3 + data[i+sx3];
}
/* Finish any remaining elements */
for (; i < length; i++) {
acc0 = acc0 + data[i];
}
return ((acc0 + acc1) + (acc2 + acc3));
}
Call test() with many combinations of elems
and stride.
For each elems and stride:
1. Call test() once to warm up the caches.
2. Call test() again and measure the read throughput(MB/s)
mountain/mountain.c

## Slide 32: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching
Fig. §6.41

## Slide 33: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 34: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register

## Slide 35: Miss Rate Analysis for Matrix Multiply
Assume:
  Cache line size = 32B (big enough for four 64-bit words)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j

## Slide 36: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > 4 bytes, exploit spatial locality
    compulsory miss rate = 4 bytes / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    compulsory miss rate = 1 (i.e. 100%)

## Slide 37: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 38: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0

## Slide 39: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
Inner loop:
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
(*,k)
(k,j)
(*,j)
Column-
wise
Column-
wise

## Slide 40: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
Inner loop:
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
(k,j)
(*,k)
(*,j)
Column-
wise
Column-
wise

## Slide 41: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
Inner loop:
Fixed
Row-wise
Row-wise
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
(k,*)

## Slide 42: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
Inner loop:
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
A
B
C
(i,*)
(i,k)
Fixed
Row-wise
Row-wise
(k,*)

## Slide 43: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 44: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700
jki | 4.8 | 4.68 | 4.65 | 4.8 | 6.84 | 15.03 | 22.78 | 29.39 | 40.39 | 57.06 | 60.54 | 63.33 | 65.61 | 67.49
kji | 4.83 | 4.72 | 4.64 | 4.69 | 6.83 | 15.1 | 22.68 | 29.18 | 40.26 | 57.02 | 60.53 | 63.34 | 65.62 | 67.53
ijk | 3.75 | 4.08 | 4.33 | 4.45 | 4.45 | 4.45 | 4.45 | 4.47 | 7.73 | 18.77 | 20.36 | 21.67 | 22.76 | 23.71
jik | 3.93 | 4.14 | 4.36 | 4.47 | 4.52 | 4.56 | 4.57 | 4.6 | 7.96 | 19.05 | 20.59 | 21.86 | 22.92 | 23.82
kij | 1.86 | 1.78 | 2.14 | 2.3 | 2.23 | 2.18 | 2.14 | 2.12 | 2.12 | 2.13 | 2.13 | 2.14 | 2.16 | 2.22
ikj | 1.78 | 1.8 | 2.12 | 2.03 | 1.96 | 1.92 | 1.89 | 1.86 | 1.86 | 1.88 | 1.89 | 1.9 | 1.91 | 1.95
ijk / jik
jki / kji
kij / ikj

## Slide 45: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 46: Example: Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n+j] += a[i*n + k]*b[k*n + j];
}

## Slide 47: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 48: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 49: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B)
for (j = 0; j < n; j+=B)
for (k = 0; k < n; k+=B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B

## Slide 50: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
First (block) iteration:
  B2/8 misses for each block
  2n/B * B2/8 = nB/4 (omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n/B blocks

## Slide 51: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 52: Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
    Input data: 3n2, computation 2n3
    Every array element used O(n) times!
  But program has to be written properly

## Slide 53: Concluding Observations
Programmer can optimize for cache performance
  How data structures are organized
  How data are accessed
    Nested loop structure
    Blocking is a general technique
All systems favor “cache friendly code”
  Getting absolute optimum performance is very platform specific
    Cache sizes, line sizes, associativities, etc.
  Can get most of the advantage with generic code
    Keep working set reasonably small (temporal locality)
    Use small strides (spatial locality)

## Slide 54: Cache Summary
Cache memories can have significant performance impact
You can write your programs to exploit this!
  Focus on the inner loops, where bulk of computations and memory accesses occur.
  Try to maximize spatial locality by reading data objects with sequentially with stride 1.
  Try to maximize temporal locality by using a data object as often as possible once it’s read from memory.

## Slide 55: Questions?

## Slide 56: One more note about caches
Suppose a multi-level cache
L1
  Access time = 4 cycles
  Miss rate = m1
  Miss penalty = p1 = average access time of L2
L2
  Access time = 11 cycles
  Miss rate = m2
  Miss penalty = p2 = average access time of L3
…

## Slide 57: One more note about caches (continued)
Average access timeL1 =
  4 + m1 × Average access time L2 =
  4 + m1 × (11 + m2 × Average access time L3)
Suppose
  Average access timeL3 = 100 cycles
  m1 = 10%, m2 = 4%
Then Average access timeL1 =
4 + 0.1 × (11 + .04 × 100)
= 4 + 0.1 × 15
= 4 + 1.5 = 5.5 cycles

## Slide 58: Multi-level memories
Same analysis can be applied to multiple levels
Three levels of on-chip cache (Core i7)
DRAM
  Possibly multi-level in cluster systems
Disk
  Holding virtual memory

## Slide 59: Questions?