## Slide 1: The Memory Hierarchy
Professor Hugh C. Lauer CS-2011, Machine Organization and Assembly Language
(Slides include copyright materials from Computer Systems: A Programmer’s Perspective, by Bryant and O’Hallaron, and from The C Programming Language, by Kernighan and Ritchie)

## Slide 2: Execution Model for Modern Computers
Fetch one instruction from memory
Increment Program Counter
Decode Instr. / Read Register(s)
Perform ONE integer operation
Access Memory
Write to Register
A highly idealized view

## Slide 3: Modern Processor Design
Execution
Functional
Units
Instruction Control
Branch
Arith
Arith
Load
Store
Instruction
Cache
Data
Cache
Fetch
Control
Instruction
Decode
Address
Instructions
Operations
Prediction OK?
Data
Data
Addr.
Addr.
Arith
Operation Results
Retirement
Unit
Register
File
Register Updates

## Slide 4: Superscalar Processor
Definition: A superscalar processor can issue and execute multiple instructions in one cycle. The instructions are retrieved from a sequential instruction stream and are usually scheduled dynamically.
Benefit: without programming effort, superscalar processor can take advantage of the instruction level parallelism that most programs have
Most modern processors are superscalar.
Intel: since Pentium (1993)

## Slide 5: Pipelined Functional Units
  Divide computation into stages
  Pass partial computations from stage to stage
  Stage i can start on new computation once values passed to i+1
  E.g., complete 3 multiplications in 7 cycles, even though each requires 3 cycles
Stage 1
Stage 2
Stage 3
long mult_eg(long a, long b, long c) {
long p1 = a*b; long p2 = a*c; long p3 = p1 * p2;
return p3; }
 | Time |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Stage 1 | a*b | a*c |  |  | p1*p2 |  | 
Stage 2 |  | a*b | a*c |  |  | p1*p2 | 
Stage 3 |  |  | a*b | a*c |  |  | p1*p2

## Slide 6: More to say about this later in course!
Much more in CS-4515, Computer Architecture Spring 2019

## Slide 7: Problem
addq %rdx, %rax
  Requires one cycle (register to register)
addq 8(%rsp), %rax
  Requires many cycles
  Depending upon type of memory!
On-chip
  2–10 cycles to local SRAM
Off-chip
  100+ cycles to DRAM

## Slide 8: Problem (continued)
All that compute power is wasted without quick access to memory
Large on-chip memories impractical
  On-chip DRAMs technologically challenging

## Slide 9: The Processor-Memory Gap
The gap widens between DRAM, disk, and Processor speeds.
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk
Fig. 6.16

## Slide 10: Solution
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality
Exploit locality in the form of caches

## Slide 11: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 12: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 13: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 14: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}
I.e., hold row number constant while looping thru columns

## Slide 15: Locality Example
Question: What about this function?
Does it have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
I.e., hold column number constant while looping thru rows

## Slide 16: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 17: Example Matrix Multiplication
Standard desktop computer, vendor compiler, using optimization flags
Both implementations have exactly the same operations count (2n3)
What is going on?
Matrix-Matrix Multiplication (MMM) on 2 x Core 2 Duo 3 GHz (double precision)
Gflop/s
160x
Triple loop
Best code (K. Goto)

## Slide 18: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}

## Slide 19: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  Widening gap between processor and main memory speeds.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 20: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy
Caches and caching principles

## Slide 21: Definition:– Cache
A small fast memory that holds a (frequently accessed) subset of items from a much larger, slower memory
Reason:–
  To approximate the performance of the fast memory while retaining the size and economic benefits of the larger memory

## Slide 22: Basic Idea
Design a cache system so that …
… most of the accesses go to the small, fast memory, …
… and those that don’t go to the small fast memory occur with sufficiently low probability that the extra cost of access does not hurt, …
… at least, not very much

## Slide 23: Caches occur everywhere in computing
Transaction processing
    Keep records of today’s departures in RAM or local storage while records of future flights are on remote database
Program execution
    Keep the bytes near the current program counter in on-chip SRAM memory while rest of program is in DRAM
File management
    Keep disk maps of open files in RAM while retaining maps of all files on disk
Game design
    Keep details of nearby environment in cache of each character
…

## Slide 24: In fact, …
Caching is, by far, THE MOST IMPORTANT TOPIC pertaining to the performance of ANY hardware or software or distributed system!

## Slide 25: Example — Virtual Memory
Definition:– Virtual memory is the illusion that each running program has its own memory space
  Separate from those of all other running programs …
  … on the same computer or different computers …
  … belonging to the same user or different users
In reality, virtual memories are stored on disk
  Yes, really slow disks!
  RAM is a cache of the frequently used “pages” of virtual memory

## Slide 26: Properties of all caches
A mechanism to recognize when something is already in the cache …
  … and use it
  Called a Cache Hit
A mechanism to recognize when something needed is not in the cache …
  … and to fetch it from the underlying large memory into the cache
  Called a Cache Miss
A policy for throwing something out of a cache …
  … to make space for cache misses
A mechanism for updating the underlying memory when cached objects change …
  … or (especially) when they are thrown out!

## Slide 27: Caches can be layered
L1 is a cache of L2 memory
  32 k-bytes, on-chip, 4 cycle access (Core i7)
L2 is a cache of L3 memory
  256 k-bytes, on-chip, 11 cycle access
L3 is a cache of DRAM
  8 megabytes, shared among 4 cores; 30-40 cycle access
DRAM is a cache of virtual memory
  N gigabytes, shared among all processes; 100’s of cycles
Processor designer’s view

## Slide 28: Caches can be layered
L1 is a cache of L2 memory
  32 k-bytes, on-chip, 4 cycle access (Core i7)
L2 is a cache of L3 memory
  256 k-bytes, on-chip, 11 cycle access
L3 is a cache of DRAM
  8 megabytes, shared among 4 cores; 30-40 cycle access
DRAM is a cache of virtual memory
  N gigabytes, shared among all processes; 100’s of cycles
Programmer’s view

## Slide 29: Memory Hierarchy — layered caches
Registers
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
cheaper
per byte
Remote secondary storage
(tapes, distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers
Main memory holds disk blocks retrieved from local disks
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from L2 cache
CPU registers hold words retrieved from L1 cache
L2 cache holds cache lines retrieved from main memory
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
costlier
per byte
Fig. 6.21

## Slide 30: Caches and Memory Hierarchies
Fundamental idea of a memory hierarchy
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit
Big Idea: The memory hierarchy creates illusion of a large pool of storage …
  … as big and (nearly) as cheap as the bottom layer
  … as (nearly) fast as the top layer
locality,

## Slide 31: Caching is all about performance …
… and probabilities

## Slide 32: Cache Performance
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a block in the cache to the processor
    includes time to determine whether the block is in the cache
  Typical numbers:
    1-4 clock cycle for L1
    10-20 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 33: Cache Performance (continued)
Average access time =
  Hit time + miss_rate × miss penalty
Example
  Hit time for L1 cache = 1 cycle
  Miss penalty for L1 cache = 10 cycles
  Miss rate = 10%
   Average access time = 1 + 0.1 * 10 = 2
Example 2
  Miss rate = 1%
   Average access time = 1 + 0.01 * 10 = 1.1

## Slide 34: Think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
Average access time:
97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 35: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)
  Stride-1 reference patterns are good (spatial locality)
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories.
See especially: §6.5

## Slide 36: Note about hit-miss probabilities
No a priori methods to predict probabilities of caches hits and misses
I.e., no way to tell in advance how well a particular caching strategy will work
  Must determine experimentally!
Benchmarks
  Standardized suites of real programs/applications for measuring performance
Used in
  Hardware design, OS design, Database design, etc.

## Slide 37: Questions?

## Slide 38: Caches in Microprocessors
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 39: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 40: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 41: Types of Cache Misses
Cold (compulsory) miss
  Cold misses occur because the cache is empty.
Conflict miss
  Most caches limit blocks at level k+1 to a small subset (sometimes a singleton) of the block positions at level k.
    E.g. Block i at level k+1 must be placed in block (i mod 4) at level k.
  Conflict misses occur when the level k cache is large enough, but multiple data objects all map to the same level k block.
    E.g. Referencing blocks 0, 8, 0, 8, 0, 8, ... would miss every time.
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache.

## Slide 42: Examples of Caching in the Hierarchy
Hardware
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB page
64-bytes block
64-bytes block
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
1
On-Chip L1
Hardware
10
On/Off-Chip L2
AFS/NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
Processor core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 43: Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.

## Slide 44: Questions?