## Slide 1: Intro to Architecture of Computers – III Pipelining
Hugh C. Lauer
Department of Computer Science
(Slides shamelessly adapted from Bryant & O’Hallaron, with additional materials from Patterson & Hennessey, “Computer Organization & Design,” revised 4th ed. and from Hennessey & Patterson, “Computer Architecture: A Quantitative Approach,” 4th ed.)

## Slide 2: Today
Analogies in real world
Pipelining in modern processors — MIPS
Pipelining in Y86
Hazards

## Slide 3: Clothes-washing analogy
Time per load:– 2 hours
Time for 4 loads:– 8 hours!
0.5 Loads/hour
Time per load:– 2 hours (still)
Time for 4 loads:– 3.5 hours!
2 loads per hour sustained rate!

## Slide 4: Real-world pipelines: car washes
Idea
  Divide process into independent stages
  Move objects through stages in sequence
  At any given times, multiple objects being processed
Sequential
Parallel
Pipelined

## Slide 5: Computational example
System
  Computation requires total of 300 picoseconds
  Additional 20 picoseconds to save result in register
  Must have clock cycle of at least 320 ps
  Can begin a new operation every cycle — i.e., every 320 ps
Combinational
logic
R
e
g
300 ps
20 ps
Clock
Delay = 320 ps
Throughput = 3.12 GIPS

## Slide 6: 3-way pipelined version
System
  Divide combinational logic into 3 blocks of 100 ps each
  Can begin new operation as soon as previous passes through stage A.
    Begin new operation every 120 ps
  Overall latency per operation increases
    360 ps from start to finish
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Delay = 360 ps
Throughput = 8.33 GIPS

## Slide 7: Pipeline diagrams
Unpipelined
  Cannot start new operation until previous one completes
3-Way Pipelined
  Up to 3 operations in progress simultaneously
Time
OP1
OP2
OP3
Time
A
B
C
A
B
C
A
B
C
OP1
OP2
OP3

## Slide 8: Operating a pipeline
Time
OP1
OP2
OP3
A
B
C
A
B
C
A
B
C
0
120
240
360
480
640
Clock
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
239
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
241
R
e
g
R
e
g
R
e
g
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
Comb.
logic
A
Comb.
logic
B
Comb.
logic
C
Clock
300
R
e
g
Clock
Comb.
logic
A
R
e
g
Comb.
logic
B
R
e
g
Comb.
logic
C
100 ps
20 ps
100 ps
20 ps
100 ps
20 ps
359

## Slide 9: Execution model for modern computers
Fetch one instruction from memory
Increment Program Counter
Read Register(s)
Perform ONE integer operation
Access Memory (optional)
Write to Register

## Slide 10: Execution model for modern computers (flipped vertically)
Read Register(s)
Perform ONE integer operation
Access Memory (optional)
Write to Register
Fetch one instruction from memory
Increment Program Counter

## Slide 11: Sequential stages
Fetch
  Read instruction from instruction memory
  Increment program counter (%rip)
Decode
  Read registers named in instruction
Execute
  Compute value or address
Memory
  Read or write data
Write Back
  Write program registers
PC
  Update program counter (incremented or jump/call/ret target)
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 12: Sequential stages
Fetch
  Read instruction from instruction memory
  Increment program counter (%rip)
Decode
  Read registers named in instruction
Execute
  Compute value or address
Memory
  Read or write data
Write Back
  Write program registers
PC
  Update program counter (incremented or jump/call/ret target)
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC
I.e., five different instructions “in flight” at the same time!

## Slide 13: Stylized processor execution stages
Instruction fetch
Instruction decode Register read
Execute arithmetic op.
Access memory
Write to register

## Slide 14: Stylized processor — not pipelined vs. pipelined
Each instruction is 1000 ps
Each instruction is 800 ps

## Slide 15: Stylized processor pipeline
Instruction fetch
Instruction decode Register read
Execute arithmetic op.
Access memory
Write to register
Register “file” can write and read in two half-cycles

## Slide 16: Questions?

## Slide 17: Today
Analogies in real world
Pipelining in modern processors — MIPS
Pipelining in Y86
Hazards

## Slide 18: Adding pipeline registers to Y86
Instruction
memory
Instruction
memory
PC
increment
PC
increment
CC
CC
ALU
ALU
Data
memory
Data
memory
Fetch
Decode
Execute
Memory
Write back
icode
,
ifun
rA
,
rB
valC
Register
file
Register
file
A
B
M
E
Register
file
Register
file
A
B
M
E
PC
valP
srcA
,
srcB
dstA
,
dstB
valA
,
valB
aluA
,
aluB
Cnd
valE
Addr
, Data
valM
PC
valE
,
valM
newPC

## Slide 19: Pipeline stages
Fetch
  Select current PC
  Read instruction
  Compute incremented PC
Decode
  Read program registers
Execute
  Operate ALU
Memory
  Read or write data memory
Write Back
  Update register file

## Slide 20: Alternate view (Hennessey & Patterson)
Memory
Access
Write
Back
Instruction
Fetch
Instr. Decode
Reg. Fetch
Execute
Addr. Calc
ALU
Instr. Memory
Reg File
MUX
MUX
Data
Memory
MUX
Sign
Extend
Zero?
IF/ID
ID/EX
MEM/WB
EX/MEM
4
Adder
Next SEQ PC
Next SEQ PC
RD
RD
RD
WB Data
Next PC
Address
RS1
RS2
Imm
MUX

## Slide 21: Visualizing pipeline behavior
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5

## Slide 22: Stylized pipeline performance

## Slide 23: Stylized pipeline performance
Assumes L1 I-cache
Assumes L1 D-cache

## Slide 24: Quantifying the speedup
Assume
    40% ALU operations
    20% branches
    30% Load operations
    10% Store operations
    No pipeline penalty
Average (non-pipelined) instruction duration = 650 ps

## Slide 25: Quantifying the speedup (continued)
Unpipelined architecture would allow variable duration instructions
    Branches much faster than Loads
Pipelined architecture requires every cycle to take exactly the same time
    Some wasted time in Branch, ALU, and Store operations
Speedup is less if there is a penalty for pipelining

## Slide 26: Quantifying the speedup (continued)
Unpipelined architecture would allow variable duration instructions
    Branches much faster than Loads
Pipelined architecture requires every cycle to take exactly the same time
    Some wasted time in Branch, ALU, and Store operations
Speedup is less if there is a penalty for pipelining
Note: If there is a penalty for including pipelining (vs. non-pipelined design), speed-up decreases

## Slide 27: Life is never that simple!
Introducing hazards
I.e., factors that interfere with full and efficient pipelining
Prevent instruction from starting or continuing on next cycle
Definition!

## Slide 28: Hazards
Structural – resource conflicts among successive instructions
    Hardware cannot support all possible combinations of instructions in rapid succession
Data – dependencies of instructions on results of other instructions
    x = a * b + c Cannot add until multiply is done
Control – branches that change instruction fetch order
    Will affect instructions that have already been fetched!

## Slide 29: Structural hazard example:– one memory port
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg

## Slide 30: Structural hazard example:– one memory port
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
Instr 3
Instr 4
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Assume combined I- and D-cache
Cannot read two different words in one cycle!

## Slide 31: Structural hazard example:– one memory port
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)
Load
Instr 1
Instr 2
stall
Instr 3
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Cycle 1
Cycle 2
Cycle 3
Cycle 4
Cycle 6
Cycle 7
Cycle 5
Reg
ALU
DMem
Ifetch
Reg
Bubble
Bubble
Bubble
Bubble
Bubble
I.e., Instr 3 “stalls” one cycle.

## Slide 32: “Harvard Architecture”
(Originally) physically separate storage and signal pathways for instructions and data
(Today) separate I-caches and D-caches

## Slide 33: Other structural hazards (examples)
Multiply
    Expensive in gates to make fully pipelined
Floating-point divide
    Very expensive to make fully pipelined
Floating-point square-root
    Prohibitively expensive to pipeline at all

## Slide 34: Structural hazards (conclusion)
Processor hardware must check
  Introduce “stalls”
Compiler should be aware
  Re-arrange compiled code

## Slide 35: Questions?

## Slide 36: Data hazard on %eax/%rax
I
n
s
t
r.
O
r
d
e
r
movl (%rsp),%rax
sub %rax, %rcx
and %rax, %rdx
or %rax, %rd1
xor %rax, %rsi
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 37: Data hazards
Extremely common
Some hardware solutions
  Special forwarding data paths
  Other extraordinary solutions
Compilers need to beware!
  Move code to minimize
  Be aware during register allocation

## Slide 38: Control hazard on jumps
I
n
s
t
r.
O
r
d
e
r
test %rax,%rax
jne <destination>
and %rax, %rdx
or %rax, %rdi
xor %rax, %rsi
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 39: Control hazard on jumps — better
I
n
s
t
r.
O
r
d
e
r
test %rax,%rax
another instruction
another instruction
jne <destination>
xor %rax, %rsi
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 40: Control hazard on jumps — even better
I
n
s
t
r.
O
r
d
e
r
test %rax,%rax
cmovnz %rsi, %rdi
cmovz %rcx, %rdi
sub $4, %rsp
xor %rax, %rsi
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Reg
ALU
DMem
Ifetch
Reg
Time (clock cycles)
IF
ID/RF
EX
MEM
WB

## Slide 41: Other control hazards
Call — PC changes on very next instruction
Ret — ditto
  Plus data hazards on stack
Architectural solutions
  Branch delay
Compiler solutions
  Careful code motion
Hardware solutions
  Speculative execution

## Slide 42: Questions?