## Slide 1: Introduction to the Architecture of Computers
Professor Hugh C. Lauer CS-2011, Machine Organization and Assembly Language
(Slides include copyright materials from Computer Systems: A Programmer’s Perspective, by Bryant and O’Hallaron, and from The C Programming Language, by Kernighan and Ritchie)

## Slide 2: Today
Before electronic computers
Logic and gates
Latches and Registers

## Slide 3: Before electronic computers
Data values represented by positions of beads
Arithmetic by manual algorithm
Data values represented by rotational positions of wheels and dials
Arithmetic by rotating wheels and gears

## Slide 4: Charles Babbage “engines”
Difference engine
Analytical engine
Data values represented by rotational positions of wheels and dials

## Slide 5: Jacquard Loom
Punched cards for controlling patterns of woven cloth
Punched cards were part of Babbage’s design for data entry and program control

## Slide 6: Punched card tabulating equipment
Late 19th century
Mid 20th century
Data stored in trays (i.e., “files”) of punched cards algorithms coded into plug-boards to operate on data, punch new cards, etc.

## Slide 7: Today
Before electronic computers
Logic and gates
Latches and Registers
Reading Assignment: §4.2

## Slide 8: Overview of Logic Design
Fundamental Hardware Requirements
  Communication
    How to get values from one place to another
  Computation
  Storage
Bits are Our Friends
  Everything expressed in terms of values 0 and 1
  Communication
    Low or high voltage on wire
  Computation
    Compute Boolean functions
  Storage
    Store bits of information

## Slide 9: Digital Signals
  Use voltage thresholds to extract discrete values from continuous signal
  Simplest version: 1-bit signal
    Either high range (1) or low range (0)
    With guard range between them
  Not strongly affected by noise or low quality circuit elements
    Can make circuits simple, small, and fast
Voltage
Time
0
1
0

## Slide 10: Computing with Logic Gates
  Outputs are Boolean functions of inputs
  Respond continuously to changes in inputs
    With some, small delay
Voltage
Time
a
b
a & b
Rising Delay
Falling Delay
a
b
out
a
b
out
a
out
out = a
&
b
out = a
|
b
out =
~
a
And
Or
Not

## Slide 11: Combinational Circuits
Acyclic Network of Logic Gates
  Continously responds to changes on primary inputs
  Primary outputs become (after some delay) Boolean functions of primary inputs
Acyclic Network
Primary
Inputs
Primary
Outputs

## Slide 12: Bit Equality and Exclusive OR
  Generate 1 if a and b are equal
Bit equal
a
b
eq
Exclusive OR
a
b
Xor
  Generate 1 if a and b are not equal

## Slide 13: Word Equality
  32-bit word size
  May be adapted to any word size
b31
Bit equal
a31
eq31
b30
Bit equal
a30
eq30
b1
Bit equal
a1
eq1
b0
Bit equal
a0
eq0
and
Eq
=
B
A
Eq
Word-Level Representation

## Slide 14: Bit-Level Multiplexor
  Control signal s
  Data signals a and b
  Output a when s=1, b when s=0
Bit MUX
b
s
a
out
bool out = (s&a)||(!s&b)

## Slide 15: Word Multiplexor
  Select input word A or B depending on control signal s
Word-Level Representation
b31
s
a31
out31
b30
a30
out30
b0
a0
out0
s
B
A
Out
MUX

## Slide 16: Decoder
Opposite of Multiplexor
Selects one of 2n outputs from n inputs
=1 if and only if AB = 00
=1 if and only if AB = 01
=1 if and only if AB = 10
=1 if and only if AB = 11

## Slide 17: Single-bit adder
+
A
B
Carry In
Carry Out
Sum
A | B | Carry In | Carry Out | Sum | 
0 | 0 | 0 | 0 | 0 | 0 + 0 + 0 = 002
0 | 0 | 1 | 0 | 1 | 0 + 0 + 1 = 012
0 | 1 | 0 | 0 | 1 | 0 + 1 + 0 = 012
0 | 1 | 1 | 1 | 0 | 0 + 1 + 1 = 102
1 | 0 | 0 | 0 | 1 | 1 + 0 + 0 = 012
1 | 0 | 1 | 1 | 0 | 1 + 0 + 1 = 102
1 | 1 | 0 | 1 | 0 | 1 + 1 + 0 = 102
1 | 1 | 1 | 1 | 1 | 1 + 1 + 1 = 112

## Slide 18: Single-bit adder (cont.)
A | B | Carry In | Carry Out | Sum | 
0 | 0 | 0 | 0 | 0 | 0 + 0 + 0 = 002
0 | 0 | 1 | 0 | 1 | 0 + 0 + 1 = 012
0 | 1 | 0 | 0 | 1 | 0 + 1 + 0 = 012
0 | 1 | 1 | 1 | 0 | 0 + 1 + 1 = 102
1 | 0 | 0 | 0 | 1 | 1 + 0 + 0 = 012
1 | 0 | 1 | 1 | 0 | 1 + 0 + 1 = 102
1 | 1 | 0 | 1 | 0 | 1 + 1 + 0 = 102
1 | 1 | 1 | 1 | 1 | 1 + 1 + 1 = 112
A
B
Cin
Cout
Sum

## Slide 19: Multi-bit adder
A0
B0
+
C0
S0
A1
B1
+
C1
S1
A2
B2
+
C2
S2
A3
B3
+
C3
S3
An-1
Bn-1
+
Cn-1
Sn-1

## Slide 20: Arithmetic Logic Unit (single-bit example)
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
OF
ZF
CF
  Combinational logic
    Continuously responding to inputs
  Control signal selects function computed
    Corresponding to four basic arithmetic/logical operations
  Also computes values for condition codes
A
L
U
Y
X
X + Y
0
A
L
U
Y
X
X - Y
1
A
L
U
Y
X
X & Y
2
A
L
U
Y
X
X ^ Y
3
A
B
A
B
A
B
A
B
Figure 4.15 (Not in our textbook)

## Slide 21: Modern Arithmetic-Logic Unit (ALU)
Combines
  Add
  Subtract
  And
  Or
  Not
  Xor
  Equality
  <
  >
  <<
  >>
  …
Outputs
  Result
  CF — Carry flag
  ZF — Zero flag
  SF — Sign flag
  OF — Overflow flag
Result developed within one cycle (300 ps)
Conspicuously absent:– multiplication & division!

## Slide 22: Questions?

## Slide 23: Today
Before electronic computers
Logic and gates
Latches and Registers

## Slide 24: Storing 1 Bit
Bistable Element
Q+
Q–
q
!q
q = 0 or 1
Vin
V1
V2

## Slide 25: Storing 1 Bit (continued)
Bistable Element
Q+
Q–
q
!q
q = 0 or 1
Vin
V1
V2
Vin
V1
V2
Vin = V2
Stable 0
Stable 1
Metastable

## Slide 26: Physical Analogy
Stable 0
Stable 1
Metastable
Stable left
Stable right
.
Metastable
.
.

## Slide 27: Storing and Accessing 1 Bit
Q+
Q–
R
S
R-S Latch
Resetting
1
0
1
0
0
1
Setting
0
1
0
1
1
0
Storing
0
0
!q
q
q
!q
Bistable Element
Q+
Q–
q
!q
q = 0 or 1

## Slide 28: 1-Bit Latch
D Latch
Q+
Q–
R
S
D
C
Data
Clock
Latching
1
d
!d
!d
!d
d
d
d
!d
0
Storing
d
!d
q
!q
!q
q
0
0

## Slide 29: Definition — Clock
A periodic signal consisting of an alternating sequence of ones and zeros at regular intervals
  E.g., 333 picoseconds in a modern 3 GHz processor
Purpose:– to control when to capture the result of a logic circuit
  E.g., an ALU consisting of AND’s, OR’s, and NOT’s
  E.g., a register or memory or other device

## Slide 30: Register
  Stores word of data
    Different from program registers seen in assembly code
  Collection of edge-triggered latches
  Loads input on rising edge of clock
I
O
Clock
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
D
C
Q+
i7
i6
i5
i4
i3
i2
i1
i0
o7
o6
o5
o4
o3
o2
o1
o0
Clock
Structure

## Slide 31: Register Operation
  Stores data bits
  For most of time acts as barrier between input and output
  As clock rises, loads input
State = x
Rising
clock

Output = x
Input = y
x

State = y
Output = y
y

## Slide 32: (Finite) State Machine
A register or latch of n bits representing the “state” of the circuit
An acyclic network of combinatorial logic to compute a new value of n bits based on the existing value of n bits
A clock signal to effect the update of the “state” to a new “state”
Combinational
Logic Circuit
Storage
Element
output
input
AND
clock
S
MUX

## Slide 33: Finite State Machine Example
  Three groups of lights to be lit in a sequence: group 1 on, groups 1 & 2 on, all groups on, all off.
  The lights are on only if the main switch is on.
  Four states: so we need two bits to identify each state.
DETOUR
Combinational
Logic Circuit
Two bit
Storage
switch
clock
2
2
out1
out2
out3
all on
grp 1,2 on
all off
grp 1 on
1
1
0
0
0
1
0,1
01
10
11
00
d[1:0]
S

## Slide 34: Register File
  Stores multiple words of memory
    Address input specifies which word to read or write
  Register file
    Holds values of program registers
    %rax, %rsp, etc.
    Register identifier serves as address
      ID 15 (0xF) implies no read or write performed
  Multiple Ports
    Can read and/or write multiple words in one cycle
      Each has separate address and data input/output
Register
file
A
B
W
dstW
srcA
valA
srcB
valB
valW
Read ports
Write port
Clock

## Slide 35: Summary
Data values stored as bits
    On wires, in memory cells, etc.
Gates are logic elements that combine values of bits to produce other bits
    And, Or, Xor, addition, subtraction, comparison, etc.
Latches capture bit values on wires and keep them until reset
    So long as power stays on
Setting of latches is triggered by a clock, which allow data into the latches only when the results of combinatorial logic elements has stabilized.

## Slide 36: Questions?
Reading Assignment: §4.2