## Slide 1: More on Memory Hierarchy
Professor Hugh C. Lauer CS-2011, Machine Organization and Assembly Language
(Slides include copyright materials from Computer Systems: A Programmer’s Perspective, by Bryant and O’Hallaron, and from The C Programming Language, by Kernighan and Ritchie)
Notes: Note:– This topic is presented in a different order from the slides.
We start with slides 1 & 2, then skip to slide 54 and continue thru the end, then back to slide 3 thru 53.

## Slide 2: Today
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy
Reading Assignment: §6.1 – §6.5
First
Preparation for Cachelab

## Slide 3: Random-Access Memory (RAM)
Key features
  RAM is traditionally packaged as a chip.
  Basic storage unit is normally a cell (one bit per cell).
  Multiple RAM chips form a memory.
Static RAM (SRAM)
  Each cell stores a bit with a four or six-transistor circuit.
  Retains value indefinitely, as long as it is kept powered.
  Relatively insensitive to electrical noise (EMI), radiation, etc.
  Faster and more expensive than DRAM.
Dynamic RAM (DRAM)
  Each cell stores bit with a capacitor. One transistor is used for access
  Value must be refreshed every 10-100 ms.
  More sensitive to disturbances (EMI, radiation,…) than SRAM.
  Slower and cheaper than SRAM.

## Slide 4: SRAM vs DRAM Summary
Trans. Access Needs Needs
per bit time refresh? EDC*? Cost Applications
SRAM 4 or 6 1X No Maybe 100x Cache memories
DRAM 1 10X Yes Yes 1X Main memories,
frame buffers
EDC = Error Detection and Correction

## Slide 5: Conventional DRAM Organization
d x w DRAM:
  d*w total bits organized as d supercells of size w bits
cols
rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
addr
data
supercell
(2,1)
2 bits
/
8 bits
/
Memory
controller
(to/from CPU)

## Slide 6: Reading DRAM Supercell (2,1)
Step 1(a): Row access strobe (RAS) selects row 2.
Step 1(b): Row 2 copied from DRAM array to row buffer.
Cols
Rows
RAS = 2
0
1
2
3
0
1
2
Internal row buffer
16 x 8 DRAM chip
3
addr
data
2
/
8
/
Memory
controller

## Slide 7: Reading DRAM Supercell (2,1)
Step 2(a): Column access strobe (CAS) selects column 1.
Step 2(b): Supercell (2,1) copied from buffer to data lines, and eventually back to the CPU.
Cols
Rows
0
1
2
3
0
1
2
3
Internal row buffer
16 x 8 DRAM chip
CAS = 1
addr
data
2
/
8
/
Memory
controller
supercell
(2,1)
supercell
(2,1)
To CPU
Rewrite row

## Slide 8: Memory Modules
: supercell (i,j)
1 GByte
memory module
consisting of
eight 128Mx8 DRAMs
addr (row = i, col = j)
Memory
controller
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
64-bit doubleword at main memory address A
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64-bit doubleword
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 9: Enhanced DRAMs
Basic DRAM cell has not changed since invention in 1966.
  Commercialized by Intel in 1970
  (except for tinier cells, more bits per sq millimeter)
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Uses a conventional clock signal instead of asynchronous control
    Allows reuse of the row addresses (e.g., RAS, CAS, CAS, CAS)
  Double data-rate synchronous DRAM (DDR SDRAM)
    Double edge clocking sends two bits per cycle per pin
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR3 (8 bits)
    By 2010, standard for most server and desktop systems
    Intel Core i7 supports only DDR3 SDRAM

## Slide 10: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs with partial (sector) erase capability
    Wears out after about 100,000 erasings.
Uses for Nonvolatile Memories
  Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
  Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
  Disk caches

## Slide 11: Traditional Bus Structure Connecting CPU and Memory
A bus is a collection of parallel wires that carry address, data, and control signals.
Buses are typically shared by multiple devices.
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus

## Slide 12: Hardware Organization — 2005 era Pentium
ISA bridge
IDE disk
Main Memory
Processor
Level 2 cache
Bridge
Moni- tor
Graphics card
USB
Key- board
Mouse
Ether- net
SCSI
Modem
Sound card
Printer
PCI bus
ISA bus
PCI Express

## Slide 13: Memory Read Transaction (1)
CPU places address A on the memory bus.
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%eax
Load operation: movl A, %eax

## Slide 14: Memory Read Transaction (2)
Main memory reads A from the memory bus, retrieves word x, and places it on the bus.
ALU
Register file
Bus interface
x
0
A
x
Main memory
%eax
I/O bridge
Load operation: movl A, %eax

## Slide 15: Memory Read Transaction (3)
CPU read word x from the bus and copies it into register %rax.
x
ALU
Register file
x
Main memory
0
A
%eax
I/O bridge
Load operation: movl A, %eax
Bus interface

## Slide 16: Memory Write Transaction (1)
CPU places address A on bus. Main memory reads it and waits for the corresponding data word to arrive.
y
ALU
Register file
Bus interface
A
Main memory
0
A
%eax
I/O bridge
Store operation: movl %rax, A

## Slide 17: Memory Write Transaction (2)
CPU places data word y on the bus.
y
ALU
Register file
Bus interface
y
Main memory
0
A
%eax
I/O bridge
Store operation: movl %rax, A

## Slide 18: Memory Write Transaction (3)
Main memory reads data word y from the bus and stores it at address A.
y
ALU
register file
bus interface
y
main memory
0
A
%eax
I/O bridge
Store operation: movl %rax, A

## Slide 19: Questions?

## Slide 20: What’s Inside A Disk Drive?
Spindle
Arm
Actuator
Platters
Electronics
(including a
processor and memory!)
SCSI
connector
Image courtesy of Seagate Technology

## Slide 21: Disk Geometry
Disks consist of platters, each with two surfaces.
Each surface consists of concentric rings called tracks.
Each track consists of sectors separated by gaps.
Spindle
Surface
Tracks
Track k
Sectors
Gaps

## Slide 22: Disk Geometry (Multiple-Platter View)
Aligned tracks form a cylinder.
Surface 0
Surface 1
Surface 2
Surface 3
Surface 4
Surface 5
Cylinder k
Spindle
Platter 0
Platter 1
Platter 2

## Slide 23: Disk Capacity
Capacity: maximum number of bits that can be stored.
  Vendors express capacity in units of gigabytes (GB), where 1 GB = 109 Bytes (Lawsuit pending! Claims deceptive advertising).
Capacity is determined by these technology factors:
  Recording density (bits/in): number of bits that can be squeezed into a 1 inch segment of a track.
  Track density (tracks/in): number of tracks that can be squeezed into a 1 inch radial segment.
  Areal density (bits/in2): product of recording and track density.
Modern disks partition tracks into disjoint subsets called recording zones
  Each track in a zone has the same number of sectors, determined by the circumference of innermost track.
  Each zone has a different number of sectors/track

## Slide 24: Recording zones
Modern disks partition tracks into disjoint subsets called recording zones
  Each track in a zone has the same number of sectors, determined by the circumference of innermost track.
  Each zone has a different number of sectors/track, outer zones have more sectors/track than inner zones.
  So we use average number of sectors/track when computing capacity.
Spindle
…

## Slide 25: Computing Disk Capacity
Capacity = (# bytes/sector) x (avg. # sectors/track) x
(# tracks/surface) x (# surfaces/platter) x
(# platters/disk)
Example:
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
Capacity = 512 x 300 x 20000 x 2 x 5
= 30,720,000,000
= 30.72 GB

## Slide 26: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
spindle

## Slide 27: Disk Operation (Multi-Platter View)
Arm
Read/write heads
move in unison
from cylinder to cylinder
Spindle

## Slide 28: Disk Structure - top view of single platter
Tracks divided into sectors
Surface organized into tracks
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 29: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 30: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 31: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 32: Disk Access – Read
After BLUE read
After reading blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 33: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 34: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 35: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 36: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 37: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 38: Disk Access Time
Average time to access some target sector approximated by :
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
Seek time (Tavg seek)
  Time to position heads over cylinder containing target sector.
  Typical Tavg seek is 3—9 ms
Rotational latency (Tavg rotation)
  Time waiting for first bit of target sector to pass under r/w head.
  Tavg rotation = 1/2 x 1/RPMs x 60 sec/1 min
  Typical Tavg rotation = 7200 RPMs
Transfer time (Tavg transfer)
  Time to read the bits in the target sector.
  Tavg transfer = 1/RPM x 1/(avg # sectors/track) x 60 secs/1 min.

## Slide 39: Disk Access Time Example
Given:
  Rotational rate = 7,200 RPM
  Average seek time = 9 ms.
  Avg # sectors/track = 400.
Derived:
  Tavg rotation = 1/2 x (60 secs/7200 RPM) x 1000 ms/sec = 4 ms.
  Tavg transfer = 60/7200 RPM x 1/400 secs/track x 1000 ms/sec = 0.02 ms
  Taccess = 9 ms + 4 ms + 0.02 ms
Important points:
  Access time dominated by seek time and rotational latency.
  First bit in a sector is the most expensive, the rest are free.
  SRAM access time is about 4 ns/doubleword, DRAM about 60 ns
    Disk is about 40,000 times slower than SRAM,
    2,500 times slower then DRAM.

## Slide 40: Logical Disk Blocks
Modern disks present a simpler abstract view of the complex sector geometry:
  The set of available sectors is modeled as a sequence of b-sized logical blocks (0, 1, 2, ...)
Mapping between logical blocks and actual (physical) sectors
  Maintained by hardware/firmware device called disk controller
  Converts requests for logical blocks into (surface,track,sector) triples
Allows controller to set aside spare cylinders for each zone.
  Accounts for the difference in “formatted capacity” and “maximum capacity”

## Slide 41: I/O Bus
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Expansion slots for
other devices such
as network adapters.

## Slide 42: Reading a Disk Sector (1)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
mouse
keyboard
Monitor
Disk
I/O bus
Bus interface
CPU initiates a disk read by writing a command, logical block number, and destination memory address to a port (address) associated with disk controller.

## Slide 43: Reading a Disk Sector (2)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
Disk controller reads the sector and performs a direct memory access (DMA) transfer into main memory.

## Slide 44: Reading a Disk Sector (3)
Main
memory
ALU
Register file
CPU chip
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Monitor
Disk
I/O bus
Bus interface
When the DMA transfer completes, the disk controller notifies the CPU with an interrupt (i.e., asserts a special “interrupt” pin on the CPU)

## Slide 45: Questions?